“Integration of RFID-RC522 Module with SPI	Protocol on A5D2X Board”
***************************************

Prepared By: Venkatesh M venkatesh.m@phytecembedded.in

Required Hardware:
******************
- Rugged Board- a5d2x
- USB	cable
- RFID RC522 module
- Patch Cards
- RFID Tags

Pin connections:

RC522 Module RB-A5D2X (mikroBUS pinouts)

    VCC PIN no: 7 VCC_3V3
      RST PIN no: 2 PB2_RST_mBUS1
     GND PIN no: 8 GND
     MISO PIN no: 5 PC29_MISO_mBUS1
     MOSI PIN no: 6 PC28_MOSI_mBUS1
      SCK	PIN no: 4 PC30_SPCK_mBUS1
       CS PIN no: 3 PD0_NPCS1_mBUS

Step1: Create a directory to download the kernel source.

$ mkdir kernel_source
$ cd kernel_source

Step2: Clone kernel with the proper branch.

$ git clone https://github.com/rugged-board/linux-rba5d2x.git
$ cd linux-rba5d2x
$ git checkout origin/linux-rba5d2x
Step3: Copy the below patch files to the kernel source directory which you got with documents.

I) 0001-Rb-a5d2x.dtsi. patch
ii) 0002-rfid-rc522_driver. patch

Step4: Apply the patch files in the kernel source
$ git am 0001-Rb-a5d2x.dtsi. patch
$ git am 0002-rfid-rc522_driver. patch

**** ( Adding Driver in kernel in static way ) ****

Step 1: First, create a folder named `rfid_rc522`
        at the following path: /drivers/misc/
Step 2: Copy the files rc522.c, rc522_api.c, and rc522_api.h to the
        directory /drivers/misc/rfid_rc522.
Step 3: vim drivers/misc/ rfid_rc522/Kconfig
config RFID_RC522
tristate "rfid RC522 for RB-A5D2x"
        default y
help
     This driver helps you to interface with RFID RC522 with RB-A5D2x.
Step 4: vim drivers/misc/ rfid_rc522/Makefile
obj-$(CONFIG_RFID_RC522)	+= rfid-rc522.o
rfid-rc522-objs	+= rc522.o rc522_api. O
Step 5: vim drivers/misc/Kconfig
source "drivers/misc/rfid_rc522/Kconfig"
Step 6: vim drivers/misc/Makefile
obj-y	+= rfid_rc522/
Step 7: Describe Hardware in a5d2x_rugged_board_common.dtsi file
flx4: flexcom@fc018000 {
atmel,flexcom-mode = <ATMEL_FLEXCOM_MODE_SPI>;
status = "disabled";
status = "okay";

pinctrl-names = "default";
pinctrl-0 = <&pinctrl_mikrobus_spi &pinctrl_mikrobus1_spi_cs &pinctrl_mikrobus1_rst>;
atmel,fifo-size = <16>;
status = "disabled";
status = "okay";
spidev@0 {
compatible = "rohm, dh2228fv";
reg = <0>;
spi-max-frequency = <500000>;
status = "disabled";
status = "okay";
};
rc522@1 {
compatible = "phytec, rfid_rc522";
reg = <1>;
spi-max-frequency = <13560000>;
status = "okay";
};
};
i2c3: i2c@600 {
compatible = "atmel, sama5d2-i2c";

Step1: Enable the toolchain.
$ . /opt/poky-tiny/2.5.2/environment-setup-cortexa5hf-neon-poky-linux-musleabi

Step6: Configure the kernel fo rugged board-a5d2x

$ make distclean
$ make clean
$ make rb_a5d2x_defconfig
$ make menuconfig

Device Drivers --->
        Misc devices --->
        <*> rfid RC522 for RB-A5D2x
$ make

Step11: After compilation of the make command.
$ cp arch/arm/boot/zImage

Note: From this location copy the zImage to BOOT partition of the SD card

$ cp arch/arm/boot/dts/ a5d2x-rugged_board.dtb
Note: "imx6ul-phytec-ruggedboard-rdk.dtb" file from this location
to the BOOT partition of the SD card and rename it as "oftree".

Bootable SD card:
***************
Follow below steps to prepare Bootable SD card:

Note: Here we will use zImage = we have compiled
Here we will use oftree = we have compiled
u-boot.bin image & BOOT.BIN = Default images

Step2: Copy kernel image(zImage), oftree image(.dtb) into the boot partition of the sdcard.
$ cp zImage /media/<username>/BOOT
$ cp oftree /media/<username>/BOOT
Step3: extract ‘tar -xvf armhf-rootfs-debian-bullseye.tar’ it into rootfs partition of SD card.
$ sudo tar -xvf rb-sd-core-image-minimal-rugged-board-a5d2x-sd1.tar.gz -C /media/<username>/rootfs/

Testing the RFID-RC522 module in Host terminal:
****************************************
Step 1: Open the terminal and follow the given steps to boot the board.

$ Sudo minicom
: ~# root
$ ls /dev/rfid_rc522_dev

Step 2: Enable the toolchain and cross-compile the rfid_rc522_dev.c	file. Then, copy the binary file (rfid_rc522_dev) to the board's	terminal.

venkatesh@phytec:~$. /opt/poky-tiny/2.5.2/environment-setup-cortexa5hf-neon-poky-linux-musleabi
venkatesh@phytec:~$ ${CC} rfid_rc522_dev.c -o rfid_rc522_dev
venkatesh@phytec:~$ python3 -mhttp.server 8080
Serving HTTP on 0.0.0.0 port 8080 ...
192.168.1.20 - - [03/Apr/2024 10:43:11] "GET /rfid_rc522_dev HTTP/1.1" 200 -

root@rugged-board-a5d2x-sd1: ~# wget 192.168.1.30:8080/rfid_rc522_dev
Connecting to 192.168.1.30:8080 (192.168.1.30:8080)
rfid_rc522_dev 100% |***************| 9536 0:00:00 ETA
root@rugged-board-a5d2x-sd1: ~# chmod 777 rfid_rc522_dev
root@rugged-board-a5d2x-sd1: ~#./rfid_rc522_dev